Speed for Free
Current state of auto-vectorization in GCC and Clang

---
The Hidden Dimension
Software gets faster by hardware getting faster
- Core counts go up
- Clocks go up
- IPC goes up
In 1997 (!) MMX started a silent revolution
- 1 op/instruction ⇒ 16 op/instruction (today)
- Not covered natively by C/C++ type system
- 90% of performance potentially left on the table by C++
Throughput = Cores x Clocks x IPC x Ops/instruction
Introduction

---
My Angle
- Motivation
- I deeply care about performance; it's also my job
- Hand-vectorization too expensive for many applications
- Masking in AVX512 and SVE2 simplifies auto-vectorization
- GCC 15 and Clang 20 enabled auto-vectorization in –O2
- Questions
- Will the compiler do all the work for me?
- Gains in simple, STL-like code blocks
- How much potential is there at all?
GCC and Clang are awesome!
Introduction

---
Recap: Vectorization = SIMD
Basic idea akin to loop unrolling:
- Fewer iterations
  (loop overhead)
- More code
More work done by each instruction
Code size similar to scalar
Introduction

---
Vectorization = SIMD
Basic idea akin to loop unrolling
- Vector sizes 2 .. 64
- "odd" iterations at the end would need special handling
Introduction

---
Linear Algebra
- Simple structures
- High gains, moderate effort
- FP operations always use
  vector units
- HPC relevant
- 16x16 matrix multiplication
- Use specialized libs for larger problem sizes!
- Expectation
- Close to 32 Flops/cycle HW limit
struct alignas(64) Matrix
{
 float data[16][16];
};
Matrix mult(const Matrix& lhs, const Matrix& rhs)
{
 Matrix result;
 for (int i = 0; i < 16; ++i) {
   for (int k = 0; k < 16; ++k) {
     float sum = 0;
     for (int n = 0; n < 16; ++n) {
       sum += lhs.data[i][n] * rhs.data[n][k];
     }
     result.data[i][k] = sum;
   }
 }
 return result;
}
Easy Mode

---
Generated Code
https://godbolt.org/z/e737edGdY
Easy Mode

---
Results
- GCC and Clang output near optimal
- Both may fail to perform pre-load optimization
- Clang -O2 better than GCC -O2
- Rating:
  79% (log scale)
- Under optimal conditions:
  100%
Easy Mode

---
Unpack and Transform
- Extract data from odd-sized struct
- Still simple 1D operation
- Data not nicely aligned to SIMD chunk
- Tail handling required
- RGB-to-grayscale conversion
- Temporary expansion to FP32 changes vector capacity
- Expectation
- Optimal: 6 cycles / iteration (16 pixels)
- Compiler will issue intermediate permutation instructions
struct RGB
{
 uint8_t red;
 uint8_t green;
 uint8_t blue;
};
void rgb2gray(uint8_t* gray,
        const RGB* rgb,
        size_t n)
{
 std::transform(
   rgb, rgb + n, gray,
   [](auto pixel) {
     float gr = 0.299f * pixel.red
        + 0.587f * pixel.green
        + 0.114f * pixel.blue;
     return static_cast<uint8_t>(gr + 0.5f);
   });
}
Moderate

---
What the Compiler Should Produce
Masking to load only 16 x 3
bytes
Tail iteration may require "shorter" mask
"permute" to pick every 3rd put into every 4th
Masking to fill leading bytes with 0
Moderate

---
Generated Code
https://godbolt.org/z/c5YeaG96s
Copyright © Efficientware GmbH, All rights reserved.
Moderate

---
Results
- GCC -O2 requires all parameters to be static / known at compile time
- Loads 3 chunks instead of just 1 (input vector larger than processing capacity)
- No masked tail handling
- Rating:
  71% of HW limit
Moderate

---
2D Operation std::find_first_of
- Innermost of nested loops
- Usually the most costly
- May be too short for vectorization
- Operations on strings
- Often, much faster solutions exist
- LibC should cover more of those
- Expectation
- Approach HW limit for long to_find
- HW limit is 64 comparisons/cycle
auto findFirstOf(
 const std::string& s,
 const std::string& to_find)
{
 auto first1 = s.begin();
 auto last1 = s.end();
 auto first2 = to_find.begin();
 auto last2 = to_find.end();
 // logic from std_algo.h's implementation
 // of std::find_first_of()
  for (; first1 != last1; ++first1)
   for (auto it = first2; it != last2; ++it)
     if (*first1 == *iter)
       return first1;
  return last1;
}
Challenging

---
Generated Code
https://godbolt.org/z/344En8nzT
Challenging

---
Results
- Clang will often not vectorize
- Regression for short,
  modest gains for large inputs
- Effective inner loop vectorization requires masking
- Vectorizing outer loop much more efficient, but also uses masks
- Rating:
  -6% .. 32% of HW limit
- Compared to LibC-like solution:
  -5% .. 18%
Challenging

---
Compacting Vectors std::remove_copy_if
- Frequent in vectorized code
- Filter, split or reformat data
- Output shall be compact to process it further with full vector efficiency
- More efficient than gather / scatter
- Breaks vector lane mapping
- More difficult than masking
- Expectation
- No auto-vectorization
- Unaligned store limit: ~3 cycles / 64B
// tell the compiler that input and output
// buffers don't overlap
float* sanitize(float* __restrict__ out,
        const float* __restrict__ in,
        size_t count)
{
 return std::remove_copy_if(
        in,
         in + count,
         out,
        [](auto v) {
        return v <= 0.f;
        });
}
Hard

---
Illustration
in
mask
out
out = _mm256_maskz_compress_ps(mask, in)
Hard

---
Generated Code
https://godbolt.org/z/xj53fG3nP
Copyright © Efficientware GmbH, All rights reserved.
Hard

---
Results
- Same performance for
  GCC & Clang, -O2 & -O3
- No auto-vectorization
- Rating:
  0% of HW limit
Hard

---
Throughput Relative to GCC -O2
		-O2		-O3
		GCC 15.2.0	Clang 21.1.3	GCC 15.2.0	Clang 21.1.3
scalar	matmul	100%	99%	173%	173%
	rgb2gray	100%	100%	100%	100%
	find /5	100%	100%	115%	114%
	find /160	100%	100%	99%	100%
	compress	100%	100%	100%	100%
matmul	auto	100%	99%	108%	108%
	auto static	100%	100%	174%	174%
	opt	100%	100%	100%	100%
rgb2gray	auto	100%	100%	99%	99%
	opt	100%	100%	99%	99%
find	auto /5	100%	94%	101%	100%
	opt inner /5	100%	100%	104%	100%
	opt outer /5	100%	100%	99%	100%
	auto /160	100%	101%	262%	260%
	opt inner /160	100%	100%	87%	88%
	opt outer /160	100%	106%	102%	100%
	LibC-style	100%	100%	100%	98%
compact	auto	100%	100%	100%	100%
	opt	100%	101%	99%	101%
Summary

---
Conclusion
- GCC vs. Clang: At most minor differences in performance
- Simple, linear loops get meaningful speedups
- Linear algebra saw biggest performance increase
- -O3 may still be required for auto-vectorization
- Speedup may (needlessly?) depend on constant propagation
- Meaningful next step: generating masked loads and stores
- Masked operations in general
- Inner / outer loop trade-offs
Summary