Speed for Free
Current state of auto-vectorization in GCC and Clang
Stefan Fuhrmann

---
The Hidden Dimension
Software gets faster by hardware getting faster
- Core counts go up
- Clocks go up
- IPC goes up
- Throughput = Cores x Clocks x IPC
Introduction

---
The Hidden Dimension
Software gets faster by hardware getting faster
- Core counts go up
- Clocks go up
- IPC goes up
In 1997 (!) MMX started a silent revolution
- 1 op/instruction ⇒ 16 ops/instruction (today)
- Not covered natively by C/C++ type system
- 90% of performance potentially left on the table by C++
Throughput = Cores x Clocks x IPC
Introduction

---
The Hidden Dimension
Software gets faster by hardware getting faster
- Core counts go up
- Clocks go up
- IPC goes up
In 1997 (!) MMX started a silent revolution
- 1 op/instruction ⇒ 16 ops/instruction (today)
- Not covered natively by C/C++ type system
- 90% of performance potentially left on the table by C++
Throughput = Cores x Clocks x IPC
x Ops/instruction
Introduction

---
My Angle
- Motivation
- I deeply care about performance; it's also my job
- Hand-vectorization too expensive for many applications
- Masking in AVX512 and SVE2 simplifies auto-vectorization
- GCC 15 and Clang 20 enabled auto-vectorization in –O2
- Questions
- Will the compiler do all the work for me?
- Gains in simple, STL-like loops
- How much potential is there at all?
GCC and Clang are awesome!
Introduction

---
Recap: Vectorization = SIMD
Basic idea akin to loop unrolling:
Introduction

---
Recap: Vectorization = SIMD
Basic idea akin to loop unrolling:
- Fewer iterations
  (loop overhead)
- More code
Introduction

---
Recap: Vectorization = SIMD
Basic idea akin to loop unrolling:
- Fewer iterations
  (loop overhead)
- More code
More work done by each instruction
Code size similar to scalar
Introduction

---
Vectorization = SIMD
Basic idea akin to loop unrolling
1. auto a0 = a[0], b0 = b[0];
2. auto a1 = a[1], b1 = b[1];
3. auto a2 = a[2], b2 = b[2];
4. auto a3 = a[3], b3 = b[3];
6. auto c0 = a0 + b0;
7. auto c1 = a1 + b1;
8. auto c2 = a2 + b2;
9. auto c3 = a3 + b3;
11. c[0] = c0;
12. c[1] = c1;
13. c[2] = c2;
14. c[3] = c3;
1. using Vec = std::array<int32_t, 4>;
 Vec a, b, c;
 for (size_t i = 0; i < 4; ++i) {
   c[i] = a[i] + b[i];
}
1. auto av = _mm_loadu_epi32(a.data()),
      bv = _mm_loadu_epi32(b.data());
 auto cv = _mm_add_epi32(av, av);
 _mm_storeu_epi32(c.data(), cv);
- Vector sizes 2 .. 64
- "odd" iterations at the end would need special handling
Introduction

---
The Repo
https://github.com/stefeff/auto-vectorization
Introduction

---
Linear Algebra
- Well-known, regular structures
- High gains, moderate effort
- FP operations always use
  vector units
- HPC & benchmark relevant
Easy Mode

---
Linear Algebra
- Well-known, regular structures
- High gains, moderate effort
- FP operations always use
  vector units
- HPC & benchmark relevant
- 16x16 matrix multiplication
- Use specialized libs for larger problem sizes!
struct alignas(64) Matrix
{
 float data[16][16];
};
Matrix mult(const Matrix& lhs, const Matrix& rhs)
{
 Matrix result;
 for (int i = 0; i < 16; ++i) {
   for (int k = 0; k < 16; ++k) {
     float sum = 0;
     for (int n = 0; n < 16; ++n) {
       sum += lhs.data[i][n] * rhs.data[n][k];
     }
     result.data[i][k] = sum;
   }
 }
 return result;
}
Easy Mode

---
Linear Algebra
- Well-known, regular structures
- High gains, moderate effort
- FP operations always use
  vector units
- HPC & benchmark relevant
- 16x16 matrix multiplication
- Use specialized libs for larger problem sizes!
- Expectation
- Close to 32 Flops/cycle HW limit
struct alignas(64) Matrix
{
 float data[16][16];
};
Matrix mult(const Matrix& lhs, const Matrix& rhs)
{
 Matrix result;
 for (int i = 0; i < 16; ++i) {
   for (int k = 0; k < 16; ++k) {
     float sum = 0;
     for (int n = 0; n < 16; ++n) {
       sum += lhs.data[i][n] * rhs.data[n][k];
     }
     result.data[i][k] = sum;
   }
 }
 return result;
}
Easy Mode

---
Generated Code
https://godbolt.org/z/e737edGdY
Easy Mode

---
Results
Flags for auto-vectorization:
-DNDEBUG -march=native -O3 -march=znver4
Flags for scalar:
-DNDEBUG -march=native -O3 -march=znver4 \
-fno-tree-vectorize
Easy Mode

---
Results
- GCC and Clang output near optimal
- GCC may fail to perform pre-load optimization
- Clang -O2 better than GCC -O2
Flags for auto-vectorization:
-DNDEBUG -march=native -O3 -march=znver4
Flags for scalar:
-DNDEBUG -march=native -O3 -march=znver4 \
-fno-tree-vectorize
Easy Mode

---
Results
- GCC and Clang output near optimal
- GCC may fail to perform pre-load optimization
- Clang -O2 better than GCC -O2
- Rating:
  75% (log speedup : log optimal)
- Under optimal conditions:
  100%
Flags for auto-vectorization:
-DNDEBUG -march=native -O3 -march=znver4
Flags for scalar:
-DNDEBUG -march=native -O3 -march=znver4 \
-fno-tree-vectorize
Easy Mode

---
Unpack and Transform
- Extract data from odd-sized struct
- Still simple 1D operation
- Data not nicely aligned to SIMD chunk
- Tail handling required
1. RGB-to-grayscale conversion
2. Temporary expansion to FP32 changes vector capacity
3. Expectation
4. Optimal: 6 cycles / iteration (16 pixels)
5. Compiler will issue intermediate permutation instructions
Moderate

---
Unpack and Transform
- Extract data from odd-sized struct
- Still simple 1D operation
- Data not nicely aligned to SIMD chunk
- Tail handling required
- RGB-to-grayscale conversion
Temporary expansion to FP32 changes vector capacity
1. Expectation
2. Optimal: 6 cycles / iteration (16 pixels)
3. Compiler will issue intermediate permutation instructions
1. struct RGB
   {
    uint8_t red;
    uint8_t green;
    uint8_t blue;
   };
   void rgb2gray(uint8_t* gray,
           const RGB* rgb,
           size_t n)
   {
    for (size_t i = 0; i < n; ++i) {
2. auto& pixel = rgb[i];
3. float gr = 0.299f * pixel.red
4. + 0.587f * pixel.green
5. + 0.114f * pixel.blue;
6. gray[i] = static_cast<uint8_t>(gr + 0.5f);
7. }
   }
Moderate

---
Unpack and Transform
- Extract data from odd-sized struct
- Still simple 1D operation
- Data not nicely aligned to SIMD chunk
- Tail handling required
- RGB-to-grayscale conversion
- Temporary expansion to FP32 changes vector capacity
- Expectation
- Optimal: 6 cycles / iteration (16 pixels)
- Compiler will issue intermediate permutation instructions
1. struct RGB
   {
    uint8_t red;
    uint8_t green;
    uint8_t blue;
   };
   void rgb2gray(uint8_t* gray,
           const RGB* rgb,
           size_t n)
   {
    for (size_t i = 0; i < n; ++i) {
2. auto& pixel = rgb[i];
3. float gr = 0.299f * pixel.red
4. + 0.587f * pixel.green
5. + 0.114f * pixel.blue;
6. gray[i] = static_cast<uint8_t>(gr + 0.5f);
7. }
   }
Moderate

---
What the Compiler Should Produce
Masking to load only 16 x 3
bytes
Tail iteration may require "shorter" mask
"permute" to pick every 3rd put into every 4th
Masking to fill leading bytes with 0
Moderate

---
Generated Code
https://godbolt.org/z/c5YeaG96s
Copyright © Efficientware GmbH, All rights reserved.
Moderate

---
Results
Moderate

---
Results
- Only minor differences between
  GCC and Clang, -O2 and -O3
- Loads 3 chunks instead of just 1 (input vector larger than processing capacity)
- No masked tail handling
Moderate

---
Results
- Only minor differences between
  GCC and Clang, -O2 and -O3
- Loads 3 chunks instead of just 1 (input vector larger than processing capacity)
- No masked tail handling
- Rating:
  70% of HW limit
Moderate

---
2D Operation std::find_first_of
- Innermost of nested loops
- Usually the most costly
- May be too short for vectorization
Challenging

---
2D Operation std::find_first_of
- Innermost of nested loops
- Usually the most costly
- May be too short for vectorization
- Operations on strings
- Often, much faster solutions exist
- LibC should cover more of those
auto findFirstOf(
 const std::string& s,
 const std::string& to_find)
{
 auto first1 = s.begin();
 auto last1 = s.end();
 auto first2 = to_find.begin();
 auto last2 = to_find.end();
 // logic from glibc std_algo.h's implementation
 // of std::find_first_of()
  for (; first1 != last1; ++first1)
   for (auto it = first2; it != last2; ++it)
     if (*first1 == *iter)
       return first1;
  return last1;
}
Challenging

---
2D Operation std::find_first_of
- Innermost of nested loops
- Usually the most costly
- May be too short for vectorization
- Operations on strings
- Often, much faster solutions exist
- LibC should cover more of those
- Expectation
- Approach HW limit for long to_find
- HW limit is 64 comparisons/cycle
auto findFirstOf(
 const std::string& s,
 const std::string& to_find)
{
 auto first1 = s.begin();
 auto last1 = s.end();
 auto first2 = to_find.begin();
 auto last2 = to_find.end();
 // logic from glibc std_algo.h's implementation
 // of std::find_first_of()
  for (; first1 != last1; ++first1)
   for (auto it = first2; it != last2; ++it)
     if (*first1 == *iter)
       return first1;
  return last1;
}
Challenging

---
Generated Code
https://godbolt.org/z/344En8nzT
Challenging

---
Results
Challenging

---
Results
- Clang will often not vectorize
- Regression for short,
  modest gains for large inputs
- Effective inner loop vectorization requires masking
- Vectorizing outer loop much more efficient, but also uses masks
Challenging

---
Results
- Clang will often not vectorize
- Regression for short,
  modest gains for large inputs
- Effective inner loop vectorization requires masking
- Vectorizing outer loop much more efficient, but also uses masks
- Rating:
  -2% .. 32% of HW limit
- Compared to LibC-like solution:
  -1% .. 17%
Challenging

---
Compacting Vectors std::remove_copy_if
- Frequent in vectorized code
- Filter, split or reformat data
- Output shall be compact to process it further with full vector efficiency
- More efficient than gather / scatter
Hard

---
Compacting Vectors std::remove_copy_if
- Frequent in vectorized code
- Filter, split or reformat data
- Output shall be compact to process it further with full vector efficiency
- More efficient than gather / scatter
- Breaks vector lane mapping
- More difficult than masking
// tell the compiler that input and output
// buffers don't overlap
float* sanitize(float* __restrict__ out,
        const float* __restrict__ in,
        size_t count)
{
 return std::remove_copy_if(
        in,
         in + count,
         out,
        [](auto v) {
        return v <= 0.f;
        });
}
Hard

---
Compacting Vectors std::remove_copy_if
- Frequent in vectorized code
- Filter, split or reformat data
- Output shall be compact to process it further with full vector efficiency
- More efficient than gather / scatter
- Breaks vector lane mapping
- More difficult than masking
- Expectation
- No auto-vectorization
- Unaligned store limit: ~3 cycles / 64B
// tell the compiler that input and output
// buffers don't overlap
float* sanitize(float* __restrict__ out,
        const float* __restrict__ in,
        size_t count)
{
 return std::remove_copy_if(
        in,
         in + count,
         out,
        [](auto v) {
        return v <= 0.f;
        });
}
Hard

---
Illustration
in
mask
out
out = _mm256_maskz_compress_ps(mask, in)
Hard

---
Generated Code
https://godbolt.org/z/xj53fG3nP
Copyright © Efficientware GmbH, All rights reserved.
Hard

---
Results
Hard

---
Results
- Same performance -O2 & -O3
- Clang faster due to unrolling
- No auto-vectorization
Hard

---
Results
- Same performance -O2 & -O3
- Clang faster due to unrolling
- No auto-vectorization
- Rating:
  0% of HW limit
Hard

---
Throughput Relative to GCC -O2
Could it be worth going from GCC -O2 to -O3 or Clang?
Summary

---
Conclusion
- Clang has edge over GCC on scalar code and -O2
- Simple, linear loops get meaningful speedups
- Linear algebra saw biggest performance increase (small matrices)
Summary

---
Conclusion
- Clang has edge over GCC on scalar code and -O2
- Simple, linear loops get meaningful speedups
- Linear algebra saw biggest performance increase (small matrices)
- GCC -O3 may still be required for auto-vectorization
- GCC somewhat better at AVX512 code (auto- and hand-vectorized)
Summary

---
Conclusion
- Clang has edge over GCC on scalar code and -O2
- Simple, linear loops get meaningful speedups
- Linear algebra saw biggest performance increase (small matrices)
- GCC -O3 may still be required for auto-vectorization
- GCC somewhat better at AVX512 code (auto- and hand-vectorized)
- Meaningful next step: generating masked loads and stores
- Masked operations in general
- Inner / outer loop trade-offs
Summary